Flooring:

- Avoid rolling unattached Rollaway units over carpet runners, like used at entrance doors.  These carpet runners tend to bunch up in front of the caster wheels and make a difficult job of moving the Rollaway.

- Avoid rolling Rollaway units over doorway thresholds.  Two or more people may be required to partially lift each group of casters over the threshold.

Moving Unattached Rollaway Units:

- When moving an unattached Rollaway unit into or out of storage, make sure two panels are opened partially to help stabilize the unit.

- It is recommended to use even numbers of panels for best stability when moving the units.

- It is recommended to use a minimum of 4 panels per unattached section.

- Rollaway units with an odd number of attached panels may require (2) people to move.

Casters:

- Free standing Rollaway units require (2) casters per panel.

- Wall attached Rollaway units may only require (1) caster per panel.

Stacking:

The design guidelines for stacking (storage) of Rollaway units are as follows:

| Stacking Configuration: | Minimum Stacking Dimensions: |
| --- | --- |
| Perpendicular | Width = panel width plus 6 inches Depth = 2 inches per panel |
| Parallel | Width = 2 inches per panel Depth = panel width plus 6 inches |
| Telescoping | Width = 2 inches per panel plus 6 inches Depth = panel width plus 6 inches |

Panel Sizes:

- Standard Panel Size is 36” wide x 72” high (measured from hinge center to hinge center)

with overall height including the casters.

Minimum Panel Width = 27-7/8 inches (measured from hinge center to hinge center).

Maximum Panel Width = 36 inches (measured from hinge center to hinge center).

Note:

Configurations which do not meet the guidelines stated above must be approved by Dynaflair Engineering before the job is released.