# Design Specification

General contractor to furnish and install Dynaflair Mini-Shutter in prepared opening.

Curtain to be insulated.

Tubular bottom bar with cylinder lock.

Operation to be  (push up) (crank)(motor) mounted on the (right) (left).

Contact Dynaflair Corporation at (813) 248-8100. No equals will be accepted.

ARCHITECHURAL SPECIFICATION

PART 1 GENERAL

A.   Aluminum Mini Shutter

- B.   Related Sections:  Section 08350 Folding Grilles: Section 16000 Electrical.

1.02 SUBMITTALS

- Submit manufacturer’s product data, specifications, installation instructions, shop drawings with layouts, fabrication and installation details, and samples including finish

- Show wiring for power and controls. Clearly indicate manufactures wiring and field installed wiring.

1.03  QUALITY ASSURANCE

A.    Provide components from a single manufacturer.

.              B.    Field measure openings before fabrication.

- 2.01   MANUFACTURER

A.   Provide Mini Shutters manufactured by Dynaflair Corporation, 8147 Eagle Palm Drive,                                                         bbbbRiverview, Florida USA (813) 248-8100

  - MATERIAL:

A.   Slats: Double formed aluminum 0.28mm 1 ¾” wide slats filled with low density

Polyurethane foam.

B.    Finish: Double layer polyamide coating (after a coating of primer on both sides) which

gives the surface an orange peel finish according to ECCA, ASTM and DIN standards.

Standard color white.

C.    Hood and End Plate: Roll formed aluminum.

7” X 7” – for shutters up to 7’ high

8” X 8” - for shutters up to 9’ high

10” X 10”-for shutters up to 11’ high

- Finish: Powder coat polyurethanic laquer color white.

- Guides: Extruded aluminum 2 ½” X 7/8” with felt inserts, color white.

- Bottom Bar: Manufacturers standard with keyed lock.

- Operation:  Push up operation standard on units up to up to 35 square feet, crank operation

on units to 60 square feet.  Motors available on all models.

  - INSTALLATION:

- Install in accordance with manufacturers instructions and project shop drawings.

- Adjust to ensure smooth operation and clean surface.